## Slide 1: Traffic Light Challenge
Two examples …
... and a bunch of other things.

## Slide 2: Remember:
Your challenge is…
To design and implement a Racket / Arduino traffic light system
Demonstratewhat you know about Racked, arduino, design, states, etc.

## Slide 3: Some starting points: ASIP
Controlling Arduino
  Remember the Arduino workshop?
  AsipMain.rkt
#lang racket
(require "AsipMain.rkt”)
(define setup (lambda ()
(open-asip)
(set-pin-mode 13 OUTPUT_MODE)
))
(define mainLoop (lambda()
(digital-write 13 HIGH)
(sleep 1)
(digital-write 13 LOW)
(sleep 1)
(mainLoop)
))

## Slide 4: Lights Version 1
Simple repeating light sequence:
  Red
  Red + Orange
  Green
  Orange
How can we represent this sequence in Racket?
(define lightSeq
(list
(list 1 0 0 )
(list 1 1 0)
(list 0 0 1)
(list 0 1 0)
))

## Slide 5: Cycle through states
Current state:
  (first lightSeq)
State change:
  Remove first
  Add to end of list!
(define lightCycle (lambda (seq)
(cond [(not (empty? seq))
(setLights lights (first seq))
(sleep 1)
(lightCycle
(append (rest seq)
(list (first seq))
)
)]
) ) )

## Slide 6: Version 2: making it reactive
How can we make the lights respond to user input?
Add a button
Button presses trigger state transitions
(require
"AsipButtons.rkt")
(on-button-pressed 5
(lambda ()
(printf “Press”)))

## Slide 7: FSMs in Racket
Remember tabular representation of FSM:

## Slide 8: Representation in Racket
Use the “hash” structure
  Implementation of ‘tables’ or ‘mappings’
(define stateTable
(hash
  1 (hash "b" 2 "e" 1 )
2 (hash "b" 3 "e" 1 )
3 (hash "b" 4 "e" 1 )
4 (hash "b" 1 "e" 1 )
) )

## Slide 9: Manipulating state
Record the state
Figure out next
Update current
Set lights
(define currentState 1)
(getNextState state event)
(gotoNextState event)
(outputCurrentState)

## Slide 10: Finally…
Sometimes useful to test without an Arduino
GUI simulation
LEDs connected to pins 7, 8, 9, 11, 12, 13.
Buttons connencted to pins 5 & 6
Same functions as AsipMain
(require
"AsipSimulated.rkt“)

## Slide 11: Summary
Examples:
  SimpleSingleTraffic.rkt & DoubleTraffic.rkt
Files:
  AsipMain.rkt & AsipUtilities.rkt
  AsipButtons.rkt
  AsipSimulated.rkt & AsipButtonsSimulated.rkt